## Slide 1: How to Make Almost Everything
Digital Electronic Design (2/2)
Brice PARILUSYAN
PhD Student
brice.parilusyan@gmail.com

## Slide 2: Course overview
01|
02|
03|
Logic gates
Sequential logic
Digital electronic
04|
Practice

## Slide 3
Logic gates
Digital electronic basics
Main gates
Exercises

## Slide 4
1|
Logic gates
Digital electronic basics
Digital Waveform
Data shape
Transistor assembly

## Slide 5
1|
Logic gates
Definition:
Digital signal is the result of the conversion of a continuous signal to a discrete signal. In digital electronics, there are only two voltage states present at any point within a circuit, high or low.
The high and low states can be represented as true and false statements, which are used in Boolean logic. In most cases, high equals true and low equals false.
Digital waveform

## Slide 6
1|
Logic gates
Definition :
Binary is a data encoding that uses the only 2 states of digital electronics (High and low).
Octal is a data encoding on base 8. It means there are only 8 digits allowed. 0,1,2,3,4,5,6,7
Hexadecimal is a data encoding on base 16. It means there are 16 digits allowed. 0,1,2,3,4,5,6,7
,8,9,A,B,C,D,E,F
Data shape

## Slide 7
1|
Logic gates
Definition :
A logic gate is a component assembly designed to output specific signals depending on the input. Most of them are made from transistors. Logic gates are the building block of digital electronics
Transistor assembly

## Slide 8
1|
Logic gates
Main gates
Truth table
NOT gates
OR gates
AND gates
NOR gates
NAND gates
XOR gates

## Slide 9
1|
Logic gates
Definition :
A truth table is a mathematical table used in logic that expresses all the results of a function, considering the entry values possibilities.
In this example, we have the truth table of an unknown function. What can extract from it is the result considering the two-entry p and q
Truth table

## Slide 10
1|
Logic gates
Definition :
NOT gates, or invertor gates, is a gate that invert any signals use as input.
NOT gates

## Slide 11
1|
Logic gates
Definition :
OR gates output a high level in any case except if all the inputs are low.
OR gates

## Slide 12
1|
Logic gates
Definition :
AND gates output a low level in any case except if all the inputs are high.
AND gates

## Slide 13
1|
Logic gates
Definition :
NOR gates are OR gates with all the output inverted.
NOR gates

## Slide 14
1|
Logic gates
Definition :
NAND gates are AND gates with all the output inverted.
NAND gates

## Slide 15
1|
Logic gates
Definition :
XOR gates are OR gates with all the output inverted and an exclusive expression added. It means if all the inputs are high, then the output is low automatically.
XOR gates

## Slide 16
1|
Logic gates
Exercises

## Slide 17
1|
Logic gates
Define the truth table of the following circuit :

## Slide 18
1|
Logic gates
Define the truth table of the following circuit :

## Slide 19
Sequential logic
Logic gates assembly
Practice

## Slide 20
2|
Sequential logic
Logic gates assembly
SR Latch
D Latch
D Flip-flop
JK Flip-flop

## Slide 21
2|
Sequential logic
Definition :
Sequential logic refer to circuits who compensate for a lack of memory from the combinational circuit. They can store information.
An SR latch is a sequential logic circuit that stores a bit of information.
SR latch

## Slide 22
2|
Sequential logic
Definition :
D latch is an upgrade version of the SR-latch. It eliminates the “illegal” input states. With a D latch, you can write information only if you put the enable pin to high.
D latch

## Slide 23
2|
Sequential logic
Definition :
D type flip-flop is referencing to a D latch logic gates, pulsed by a periodic signal named clock.
D flip-flop

## Slide 24
2|
Sequential logic
Description :
JK flip-flop is the last kind of assembly. A JK flip-flop resembles an SR flip-flop, where J acts like S and K acts like R. Likewise, it has a set mode (J = 1, K = 0), a reset mode (J = 0, K = 1), and a hold mode (J = 0, K = 0). However, unlike the SR flip-flop, which has an indeterminate mode when S = 1, R = 1, the JK flip-flop has a toggle mode when J = 1, K = 1. Toggle means that the Q and no-Q outputs switch to their opposite states at each active clock edge.
JK flip-flop

## Slide 25
2|
Sequential logic
Practice

## Slide 26
2|
Sequential logic
Recreate a D-latch

## Slide 27
2|
Sequential logic
Add a NE555 to generate a clock to E !

## Slide 28
Digital electronic
Binary
Digital arithmetic

## Slide 29
3|
Digital electronic
Binary
Binary conversion
Octal & Hexadecimal
Adding
Subtracting
Clock
ASCII

## Slide 30
3|
Digital electronic
Exercises :
1) Represent the following base 10 numbers as a byte : 208, 122, 42, 17,70,13
2) Represent the following byte as base 10 numbers : 00110111, 01001110, 00100000, 01110101, 11001000
Binary conversion

## Slide 31
3|
Digital electronic
Exercise :
1) Convert the following base 10 numbers in octal then hexadecimal: 208, 122, 42, 17,70,13
2) Convert the following byte octal and hexadecimal: 00110111, 01001110, 00100000, 01110101, 11001000
Octal & Hexadecimal

## Slide 32
3|
Digital electronic
Definition :
Adding binary numbers is just like adding decimal numbers. Whenever the result of adding one column of numbers is greater than one digit, a 1 is carried over to the next column to be added.
Example :
01100101 + 00001101
01010101 + 10101010
11001010 + 00101101
Adding

## Slide 33
3|
Digital electronic
Definition :
Binary subtraction is tedious, it is like decimal subtraction but can be confusing. The trick to subtracting binary numbers is to invert the subtractor and add 1 to it. Then add the result with the subtracted byte. The supplementary bit is the sign bit (0 = -, 1 = +).
My personal tips -> be lazy, convert it in base 10, subtract then convert the result in binary
Subtracting

## Slide 34
3|
Digital electronic
Definition :
The clock is a periodic digital signal who manages the timing of the operations. Each CPU need to have a clock frequency (generally created by a crystal). When two devices work together, they need to share their clock pulse to be synchronous. Higher is the clock frequency, Higher is the processing speed of the component
Clock

## Slide 35
3|
Digital electronic
Definition :
American Standard Code for Information Interchange (ASCII) is an alphanumeric code used to transmit letters, symbols, numbers, and special non-printing characters between computers and computer peripherals (such as printers and keyboards). ASCII consists of 128 different 7-bit codes.
ASCII

## Slide 36
3|
Digital electronic
Digital arithmetic
Logic adder
Logic subtractor
Practice

## Slide 37
3|
Digital electronic
Definition :
A logic adder is a kind of circuit called arithmetic logic unit (ALU). Adders are made from XOR/AND gates or NOR/AND gates. The most complicated operation a full adder can do is 1+1. But combined with other adders, it can add more complex numbers.
Logic adder

## Slide 38
3|
Digital electronic
Definition :
A logic adder is a kind of circuit called arithmetic logic unit (ALU). It is possible to use the circuit to perform adding as subtracting. The XOR doesn’t modify anything for adding, but invert the binary number for subtracting. Then this number is added to 1 and used to perform and adding operation.
Logic subtractor

## Slide 39
3|
Digital electronic
Create a full adder with XOR/AND gates.
Then ask other groups to merge your adders in a 4-bit adder
Practice